2.11 BSD on PiDP-11
Getting date and time at bootup from a time server

This should be done AFTER having set up networking and having checked whether ping works properly. Thanks to Jason Vanick and Johnny Billquist for this information.

To set date and time automatically during bootup, put the following line just before ntpt in /etc/rc.local:

  ntp -sf pool.ntp.org

To make sure that it is still executable, type

  chmod +x etc/rc.local

Change the last line in /etc/ntp.conf to

  server pool.ntp.org

To get the timezone for the system set up properly, first check available timezones in /usr/share/zoneinfo. Use the file name of your time zone in this directory as timezone in the command below.

Login as root

  cd /etc
  mv localtime localtime.old
  ln -s /usr/share/zoneinfo/timezone localtime